## Slide 1: Attractive Accents: The Versatile Appeal of Architectural Metal
Course # MTL102-PAC-23
Learning Units: 1 AIA LU
Notes: Attractive Accents: The Versatile Appeal of Architectural Metal

## Slide 2: Course registration
Petersen Aluminum is a Registered Provider with The American Institute of Architects Continuing Education Systems (AIA/CES). Credit(s) earned on completion of this program will be reported to AIA/CES for AIA members. Certificates of Completion for both AIA members and non-AIA members are available upon request.
This program is registered with AIA/CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product.
This presentation is protected by US and International Copyright laws. Reproduction, distribution, display and use of the presentation without written permission is prohibited.
Provider #: K031
© 2023

## Slide 3
Learning objectives
Describe multiple types of metal cladding, including roofing, wall systems, soffits, perforated panels and tiles, and how they are applied to buildings of all shapes, sizes and purposes.
Explore creative options and applications for perforated metal including hole size, shape, spacing, open space, and how it is applied including for equipment screens, aesthetic accents, acoustics, airflow and more.
Consider simulated finishes, including copper, weathered metal, wood grain, natural ore, as well as the anodized aluminum option.
Discuss examples of architectural metal applications from numerous case studies showing the varied and creative ways metal is specified and applied.
Upon completing this course you will be able to:

## Slide 4
Architectural metal panel systems offer numerous benefits
Design versatility and appeal
Variety of applications: roofs, walls, soffits, accents and more
Customization to fit unique project requirements
Various shapes, sizes, finishes
Durable, long-lasting and low-maintenance
Introduction
Notes: Ronald McDonald House, Ohio. Flush wall panels in four (4) colors (some custom), snap-seam roof, continuous cleat gold coping.
Architectural metal panels offer unparalleled design versatility and appeal. They can be used for a range of applications, from roofing and wall systems to soffits, accents, and beyond. One of the key advantages of metal panels is their ability to be customized to fit the unique requirements of a project. Metal panels come in a variety of shapes, sizes, and finishes, allowing designers to create unique and visually stunning structures. They can be used to achieve a range of looks, from sleek and modern to rustic and industrial. Additionally, metal panels are durable, long-lasting, and require minimal maintenance, making them an excellent investment for any project. Whether used as a functional component of a building or as a decorative feature, architectural metal panels are a popular choice among architects and designers for their versatility, durability, and aesthetic appeal.

## Slide 5
Roof systems
Wall systems
Soffits
Tile
Perforation
Section 1: Types of architectural metal cladding and how they are applied
Notes: This section will examine various types of metal cladding and the ways in which they are applied to buildings of all shapes, sizes, and purposes.
We will explore roof and wall panel systems, soffits, tiles, and perforated metal options..

## Slide 6
Metal roof systems
Standing seam
Steel and aluminum
Snap-seam
Mechanically seamed
Section 1: Types of architectural metal cladding and how they are applied
Notes: Limetree Beach Resort, USVI. Blue standing seam panels, .032 aluminum.
Best practice for standing seam metal roofing panels include PVDF coating for prefinished sheet metal, which can be applied to both steel and aluminum roof panels. This finish was originally developed for use in abrasive environments.

## Slide 7
Metal roof systems
Produced in factory-formed lengths
Longer lengths if formed on jobsite
Wide color range
Many colors meet LEED requirements and are Cool Roof-rated
Section 1: Types of architectural metal cladding and how they are applied
Notes: Altgeld Family Resource Center, Chicago. Snap-seam, custom color.
Architectural panels for standing seam metal roofing systems may be produced in a variety of factory-formed lengths, generally up to 55 feet. They are also available in longer lengths.
There is tremendous color variety in the marketplace for steel and aluminum roofing panels, with many meeting LEED requirements and some that are Cool Roof-rated. Check with manufacturer for special orders and warranty information.

## Slide 8
Pitch range and applications
Different types of metal roof panels have specific roof pitch ratings ranging from 1/2:12 to 3:12
Pitch affects panel selection
Regions with extreme weather conditions may necessitate a higher roof pitch
Section 1: Types of architectural metal cladding and how they are applied
Notes: First Federal Bank, Florida. Snap-seam, graphite gray finish, 24-gauge steel.
Different types of metal roof panels are designed for specific roof pitch requirements from 1/2:12 to 3:12.
It’s important to note that regions with heavy snowfall or extreme climate conditions may necessitate a higher roof pitch.

## Slide 9
Roof project review
Sevier County Utility District
Section 1: Types of architectural metal cladding and how they are applied
Notes: Sevier County Utility District, Alabama. Snap-seam in gray, standing seam in blue, flush panel in blue, 24-gauge steel.
Mechanically seamed 90-degree lock, also snap-lock for walls, both 24-gauge steel.

## Slide 10
Roof project review
Theodore Roosevelt National Wildlife Refuge
Section 1: Types of architectural metal cladding and how they are applied
Notes: Theodore Roosevelt National Wildlife Refuge, Mississippi. Mechanically seamed 90-degree roof panels, 24-gauge, simulated weathered steel finish in a 2-coat Kynar paint.

## Slide 11
Roof project review
Innovation Amphitheater
Section 1: Types of architectural metal cladding and how they are applied
Notes: Innovation Amphitheater, Georgia. Mechanically seamed 90 degrees, 24-gauge, charcoal gray finish, field-rolled panels due to panel lengths over 80 feet long.

## Slide 12
Roof project review
Shirley Ryan AbilityLab
Section 1: Types of architectural metal cladding and how they are applied
Notes: Shirley Ryan AbilityLab, Illinois. Mechanically seamed 180-degrees, 24-gauge, weathered zinc. Soffit in .032. Example of how to properly flash a “butterfly roof” with this valley. NOTE: Penetrations (vents, etc.) in the valley have been digitally removed.

## Slide 13
Roof project review
Florida Panhandle home
Section 1: Types of architectural metal cladding and how they are applied
Notes: Panhandle home, Florida. Snap-seam, dark bronze finish, in .040” aluminum for the salt exposure; this job sits directly on Intercoastal Waterway in Florida.

## Slide 14
Roof project review
Matchbox house
  Roof panels applied as wall
Section 1: Types of architectural metal cladding and how they are applied
Notes: Matchbox House, Michigan. Snap-seam used as both roof and wall panels. Note how the contractor has matched up the verticals of the roof panels to the wall panels.

## Slide 15
Metal wall systems
Single skin, not insulated
Hidden fastener
Exposed fastener
Composite
Section 1: Types of architectural metal cladding and how they are applied
Notes: Metric Apartments, Minnesota. Box rib panel in a weathered zinc finish, 22-gauge.

## Slide 16
Metal wall systems
Testing, approvals
  Types, relevance
For example …
Section 1: Types of architectural metal cladding and how they are applied

## Slide 17
Metal wall systems
Sustainability
  Environmental Product Declaration
  Recyclability
  Cool Roof ratings
  Life Cycle Assessment
  LEED points
Section 1: Types of architectural metal cladding and how they are applied

## Slide 18
Metal wall systems
Any structure is a candidate
Vertical, horizontal, diagonal
Customization: length, width, color, profile combinations
Ease of installation
Design versatility
Structural integrity, weather resistance, low maintenance, aesthetic appeal
Section 1: Types of architectural metal cladding and how they are applied
Notes: Black Diamond Car Wash, Louisiana. Decorative ribbed industrial metal wall panels, 24-gauge steel, weathered zinc finish.
Metal wall panel systems can be customized to match specific design requirements, making them a popular choice in commercial buildings, retail spaces, and even residential structures seeking a modern and sleek appearance.
These panels not only enhance overall aesthetics but also contribute to energy efficiency, noise reduction, and fire resistance.
With their remarkable strength and adaptability, industrial metal wall panel systems provide a reliable and cost-effective solution for a wide range of applications.

## Slide 19
Flush and reveal wall panels
Versatile and highly functional architectural solutions
  Seamlessly integrate into building exteriors
  Create a sleek, streamlined appearance
Durable and resilient
  Panels made from materials such as aluminum, steel, or zinc
  Durability, strength and resistance to environmental factors
Section 1: Types of architectural metal cladding and how they are applied
Notes: Kirkwood Performing Arts Center, Missouri. Flush panel, various gray finishes, 24-gauge steel.
Flush metal panel wall systems are versatile and highly functional architectural solutions that find applications in various construction projects.
These systems consist of metal panels that are seamlessly integrated into building exteriors, creating a sleek, streamlined appearance. The panels are typically made from materials such as aluminum, steel or zinc, which offer durability, strength, and resistance to environmental factors.

## Slide 20
Wall panel project review
Millennium High School
Section 1: Types of architectural metal cladding and how they are applied
Notes: Millennium High School, Arizona. Flush panel, 24-gauge, custom purple, weathered zinc, gray and silver finishes.

## Slide 21
Wall panel project review
Wichita State #3
Section 1: Types of architectural metal cladding and how they are applied
Notes: Wichita State #3, Kansas. Snap-seam roof, bone white, ribbed wall panel, silver finish, 22-gauge.

## Slide 22
Wall panel project review
Court and Walnut
Section 1: Types of architectural metal cladding and how they are applied
Notes: Court and Walnut, Ohio. Flush panel, .040 aluminum, finishes: whites, grays and silver, and a custom charcoal gray.

## Slide 23
Wall panel project review
Rennen & Beecher Flats
Section 1: Types of architectural metal cladding and how they are applied
Notes: Rennen & Beecher Flats, Ohio. Flush panel, slate gray, .040 aluminum.

## Slide 24
Wall panel project review
Freight Yard Apartments
Section 1: Types of architectural metal cladding and how they are applied
Notes: Freight Yard Apartments, Florida. Ribbed wall panel, simulated weathered steel finish, 24-gauge steel.

## Slide 25
Composite wall panel systems
Lightweight core material sandwiched between metal skins
Provides strength, durability and flatness while maintaining a lightweight structure
Used in commercial, industrial and residential buildings for exterior cladding, interior partitions and decorative elements
For example: car dealerships
Section 1: Types of architectural metal cladding and how they are applied
Notes: Johnson High School, Texas. Composite panels in silver, 24-gauge.
Composite metal wall panel systems are innovative construction materials that offer numerous benefits and find extensive applications in various industries. These panels consist of a combination of metal skins and a core material, typically made of lightweight materials like aluminum, titanium, or stainless steel. The unique composition provides exceptional strength, durability, and fire resistance while maintaining lightweight structure. Composite metal wall panel systems are widely used in commercial, industrial, and residential buildings for exterior cladding, interior partitions, and decorative elements.
They offer architects a wide range of options in terms of colors, finishes, and textures, enabling the creation of aesthetically pleasing and functional structures. Additionally, these panels provide excellent thermal and sound insulation properties, enhancing energy efficiency and occupant comfort.
Overall, composite metal wall panel systems are a versatile solution that combines aesthetic appeal, performance, and sustainability, making them an ideal choice for modern construction projects.

## Slide 26
Composite project review
Hanover Square Mall
Section 1: Types of architectural metal cladding and how they are applied
Notes: Hanover Square Mall, Illinois. Composite panel, custom white finish, rainscreen system.

## Slide 27
Composite project review
Dearing Middle School
Section 1: Types of architectural metal cladding and how they are applied
Notes: Dearing Middle School, Texas. Composite panel rainscreen system, copper penny and silver finishes.

## Slide 28
Composite project review
Athens High School
Section 1: Types of architectural metal cladding and how they are applied
Notes: Athens High School, Texas. Composite panel, custom maroon finish, also flush panels in white and silver, 24-gauge 12-inch.

## Slide 29
Metal soffit systems
Soffit panels; flush, reveal
Full vent, half vent, solid
Metal soffit systems enhance aesthetics and functionality of buildings
Clean and sleek appearance
Effectively cover the underside of roofs and elevated structures
Advantages: durability, weather resistance, low maintenance
Section 1: Types of architectural metal cladding and how they are applied
Notes: Athens High School, Texas. Flush soffit panels, white, 24-gauge, 12-inch.
Metal soffit panel systems are an innovative architectural solution that enhances the aesthetics and functionality of buildings. These systems consist of metal panels installed beneath the eaves and overhangs, creating a clean and seamless appearance while effectively covering the underside of roofs and other elevated structures. Soffit metal panels offer numerous advantages, including durability, weather resistance, and low maintenance requirements.

## Slide 30
Metal soffit project review
LaTrobe Elementary
Section 1: Types of architectural metal cladding and how they are applied
Notes: LaTrobe Elementary, Pennsylvania. 180-degree mechanically seamed roof, .032 gauge aluminum soffit, custom marquis orange finish.

## Slide 31
Metal soffit project review
Bells Mill
Section 1: Types of architectural metal cladding and how they are applied
Notes: Bells Mills, Maryland. Vented aluminum soffit.

## Slide 32
Metal soffit project review
Lake Belton High School
Section 1: Types of architectural metal cladding and how they are applied
Notes: Lake Belton High School, Texas. Flush soffit, copper penny finish, 22-gauge steel.

## Slide 33
Metal tile systems
Stamped not roll-formed
Straightforward installation
Versatile and appealing for modern architectural design
Combines durability and strength of metal with elegance of tiles
Customization:
  Color combinations
  Unique and personalized designs
Section 1: Types of architectural metal cladding and how they are applied
Notes: MSP Airport, Minnesota. Cupped tile, 24-gauge steel, finishes: Various greens and a custom aged copper.
A metal tile wall panel system is a highly versatile and aesthetically appealing solution for modern architectural design. This innovative system combines the durability and strength of metal with the elegance and timeless beauty of tiles. Each panel is meticulously crafted to provide a seamless and precise installation, creating a sleek and polished look. The metal tile system offers a wide range of customization options, allowing architects and designers to create unique patterns, textures, and color combinations.

## Slide 34
Tile project review
Mosaic Apartments
Section 1: Types of architectural metal cladding and how they are applied
Notes: Mosaic Apartments, Minnesota. Stamped cupped tiles, finishes: various grays, 24-gauge steel.

## Slide 35
Tile project review
NISD Natatorium Aquatic Center
Section 1: Types of architectural metal cladding and how they are applied
Notes: NISD Natatorium Aquatic Center, Texas. Stamped flat tile, steel, custom “bright blue” finish.

## Slide 36
Tile project review
Children’s Museum + Theatre
Section 1: Types of architectural metal cladding and how they are applied
Notes: Children’s Museum + Theatre, Maine. Flat tile, .032 aluminum, finishes: white, grays, and blue.

## Slide 37
Tile project review
Deignan House
Section 1: Types of architectural metal cladding and how they are applied
Notes: Deignan House, Pennsylvania. Cupped tile, steel, bright annealed finish.

## Slide 38
Perforated metal
Innovative architectural tool
Functionality and aesthetic appeal
Precisely created perforations
Visually striking patterns
Perforations’ many purposes:
  Enhancing ventilation
  Providing natural light diffusion
  Reducing noise transmission
  Disguising eyesores
  Architectural flair
Section 1: Types of architectural metal cladding and how they are applied
Notes: Ballet Memphis, Tennessee. Perforated corrugated natural copper, also snap-seam roof panels installed as wall panels.
Perforated metal wall panel systems are innovative architectural solutions that combine functionality with aesthetic appeal. These panels consist of sheets of metal with precisely designed perforations, creating a visually striking pattern while allowing for various functional benefits. The perforations serve multiple purposes, such as enhancing ventilation, providing natural light diffusion, and reducing noise transmission.

## Slide 39
Hole sizes
Varying the hole size allows for different aesthetic effects and functional purposes
Smaller holes can create visually appealing patterns or textures on surfaces like walls or ceilings
Larger holes can be used for ventilation or light diffusion in architectural designs
Hole size enables customization and adaptability
Section 2: Creative options and applications of perforated metal

## Slide 40
Hole spacing and open space
Open space adds depth, dimension, interest
Adjusting spacing allows control over light, air, sound, or liquid passage
Suitable for sunshades, privacy screens, acoustic panels, filtration systems and more
Section 2: Creative options and applications of perforated metal
Notes: The Charles condominiums, Atlanta. Perforated 7.2 panel, .040 aluminum, weathered zinc finish.
The spacing between the holes and the resulting open space in perforated metal are crucial aspects that contribute to its functionality and performance. By adjusting the spacing, designers can control the amount of light, air, sound, or liquid that passes through the perforations. This makes perforated metal suitable for applications such as sunshades, privacy screens, acoustic panels, filtration systems, and more. The open space created by the perforations can also add depth, dimension, and visual interest to architectural facades or interior elements, giving them a contemporary and dynamic appearance.

## Slide 41
Perforated metal applications
Creates visually appealing enclosures
Hide or camouflage mechanical equipment such as a/c units, generators, utility boxes
Sleek, modern look
Protects equipment from weather
Allows for proper ventilation, airflow
Introduce patterns, textures, interest
Play of light and shadow adds depth, dynamics
Section 2: Creative options and applications of perforated metal
Notes: The University of Mississippi Medical Center, Mississippi. Perforated aluminum ribbed/horizontal wall panels in silver and blue finishes.
Perforated metal cladding finds numerous applications in different industries and sectors, primarily due to its functional and aesthetic benefits. One common application is as equipment screens. Perforated metal panels can be used to create visually appealing enclosures that hide or camouflage mechanical equipment such as air conditioning units, generators, or utility boxes. These screens not only provide a sleek and modern look to the building exterior but also serve the practical purpose of protecting the equipment from weather elements while allowing for proper ventilation and airflow.

## Slide 42
Perforated metal applications
Acoustics in concert halls, auditoriums and large spaces
  Control sound, improve acoustics
  Absorb and diffuse sound waves, reducing echoes
  Enhancing overall sound quality within the space
Regulating airflow for efficient ventilation, air distribution, and temperature control
Section 2: Creative options and applications of perforated metal
Notes: Eloy City Hall, Arizona. Perforated 7.2 panel, aged copper finish.
Perforated metal cladding also serves functional purposes, particularly in the realms of acoustics and airflow management. In acoustic applications, perforated metal panels are often used in concert halls, auditoriums, or other large spaces to control sound reflections and improve acoustics. The perforations help to absorb and diffuse sound waves, reducing echoes and enhancing the overall sound quality within the space. Similarly, in HVAC systems or industrial settings, perforated metal cladding can be utilized to regulate airflow, allowing for efficient.

## Slide 43
Perforated metal project review
Westfield Ninth Grade Center
Section 2: Creative options and applications of perforated metal
Notes: Westfield Ninth Grade Center, Texas. Perforated rib panels, charcoal gray finish, .040 aluminum.

## Slide 44
Perforated metal project review
Wichita State #7
Section 2: Creative options and applications of perforated metal
Notes: Wichita State #7, Kansas. ribbed panels, .050 aluminum.

## Slide 45
Perforated metal project review
Desert Diamond Casino Parking
Section 2: Creative options and applications of perforated metal
Notes: Desert Diamond Casino Parking, Arizona. Perforated ribbed panel, .040-gauge aluminum, silver finish.

## Slide 46
Perforated metal project review
Best Funeral Services
Section 2: Creative options and applications of perforated metal
Notes: Best Funeral Services, Arizona. Perforated ribbed panel, .040-gauge, 22% open space, red finish.

## Slide 47
Perforated metal project review
Moving Everest Charter School
Section 2: Creative options and applications of perforated metal
Notes: Moving Everest Charter School, Chicago. 7/8-inch corrugated panel, charcoal finish, hole specs: 3/8-in. on 9/16-in. centers.
Perforated corrugated installed 4 inches in front of the images of children. NOTE: Graphics of children are NOT within the manufacturer’s scope of capabilities.

## Slide 48
Simulated finishes
Zinc
Copper penny
Weathered copper
Weathered steel
Weathered zinc
Wood grain
Ore
Section 3: Simulated finishes
Notes: Simulated finishes include:
zinc
copper
weathered metal
wood grain
natural wood grain
natural ore
as well as the anodized aluminum option to paint.

## Slide 49
Simulated finishes
Enhance aesthetic appeal
Weathered metal finishes provide rustic and industrial look
Wood grain finishes offer a natural, organic feel
Natural ore finishes mimic the raw beauty of minerals and stones
Creative possibilities for architects and designers
Section 3: Simulated finishes
Notes: Mino-Bimaadiziwin Apartments, Minnesota. Flush panels, 22-gauge, custom wood grain finish, which closely resembles wood milled from white cedar trees.

## Slide 50
Describe the multiple types of metal cladding, including roofing, wall systems, soffits, perforated panels and tiles, and how they are applied to buildings of all shapes, sizes and purposes.
Explore creative options and applications of perforated metal including hole size, shape, spacing, open space, and how it is applied as equipment screens, aesthetic accents, acoustics and to aid airflow.
Consider simulated finishes, including copper, weathered metal, wood grain, natural ore, as well as anodized aluminum option to paint.
Discuss examples of architectural metal applications from numerous case studies showing the varied and creative ways metal is specified and applied.
Learning objectives recap
Now that you have completed this course, you will be able to:

## Slide 51: Thank you for your time. This concludes the American Institute of Architects (AIA) Continuing Education System (CES) course.